## Slide 1: T-Mobile WFC Handover to VoNR/LTE
Feb 2022
Noshad Bagha Uday Dave

## Slide 2: Handover Tests – WFC  Cellular & Cellular  WFC
Profile 1-3: Multi Handover
Profile 4: IP Impairments
Profile 5: Walk out of the WiFi Coverage
Profile 6: Walk in to WFC Coverage

## Slide 3: Multiple handovers - Profile 1 and 2
Testing begins with device connected to TMO Cellular Network
WiFi signal is presented to device for registration before test begins
Signal is presented at high, mid and low values at various 20 second intervals for RSSI and RSRP
KPIs:
Handover success rate
Cellular and WFC MOS is averaged together
Chart: Profile 1: Full Range Cellular and WiFi
| Location 1 | Location 2 | Location 3
WiFi | -88 | -75 | -88
LTE/NR | -75 | -88 | -75
Chart: Profile 2: Cellular Low and Full Range WiFi
| Location 1 | Location 2 | Location 3 | Location 4
WiFi | -88 | -78 | -78 | -88
LTE/NR | -84 | -87.5 | -89 | -84
WiFi | -88 | -78 | -78 | -88
LTE/NR | -84 | -87.5 | -89 | -84

## Slide 4: Multiple handovers - Profile 3
Testing begins with device on active WFC
TMO Cellular signal is presented to device for registration before test begins
Signal is presented at mid and low values at various 20 second intervals for RSSI and RSRP
KPIs:
Handover success rate
Cellular and WFC MOS is averaged together
Chart: Profile 3: WiFi Full Range to Cellular HO Region
| Location 1 | Location 2 | Location 3
WiFi | -75 | -88 | -75
LTE/NR | -88 | -84 | -88

## Slide 5: IP impairment handovers - Profile 4
Testing begins with device on active WFC
WiFi signal is presented at -65 RSSI while IP impairments are increased every 20 seconds
NR/LTE RSRP is static at -115 dBm for duration of test
KPIs:
  Call Performance (AFR and DCR)
  Speech Quality between and after HO (MOS)
Chart: Profile 4: Increasing IP Impiarment while in WFC until HO
| Location 1 | Location 2 | Location 3
WiFi | -10 | -10 | -10
Packet-Loss | 0.01 | 0.2 | 0.4

## Slide 6: Walk In/Out of WiFi coverage- Profile 5 & 6
Testing begins with device on active WFC
TMO Cellular signal is presented to device for registration before test begins
KPIs:
  Speech Latency (Continuous audio file)
  Speech Quality (MOS)
Chart: Profile 5: Walk out of WFC to Cellular
| Location 1 | Location 2 | Location 3
WiFi | -65 | -75 | -83
NR/LTE | -75 | -75 | -75
WiFi | -65 | -75 | -83
NR/LTE | -75 | -75 | -75
Chart: Profile 6: Walk into WFC Coverage
| Location 1 | Location 2 | Location 3
WiFi | -89 | -83 | -77
NR/LTE | -88 | -88 | -88

## Slide 7
Thank you!

## Slide 8: Handover Tests – WFC  Cellular & Cellular  WFC
Profile 1-3: Multi Handover
  To ensure that the device can handover multiple times in a single call at network defined settings
  Profile1 and 2 WFC to Cellular
  Profile 3 is Cellular to WFC
  4 iterations of the same sequence of attenuations per profile
  Test Time: ~60 mins
  KPIs measured: Handover Success Rate and Speech Quality (MOS)
Profile 4: IP Impairments
  To measure the effects of IP impairments on WFC to Cellular handovers
  WFC to Cellular Only
  1% Packet Loss increase up to 40% and 2 msec of Jitter per 20 secs
  Iterations: 2 times
  Test Time: ~30 Mins
  KPIs measured: Call Performance (AFR and DCR) and Speech Quality between and after (MOS)
Profile 5: Walk out of the WiFi Coverage
  To ensure handovers take place when WiFi signal decreases
  WFC to Cellular only
  Iterations: 2 times
  Test Time: ~30 Mins
  KPI Measured: Speech Latency (Continuous audio file) and Speech Quality (MOS)
Profile 6: Walk in to WFC Covera
  To ensure handovers take place when user moves from Cellular to stronger WiFi signal
  Cellular to WFC only
  Iterations: 2 times
  Test Time ~30 mins
  KPI Measured: Speech Latency (Continuous audio file) and Speech Quality (MOS)
All tests performed with Cellular preferred selected